## Slide 1: Lecture 15: Introduction to Control
Introduction to control
Block diagram reduction

## Slide 2: Introduction to Control
So far we have modeled systems and analyzed their time-response behavior
Specifications may exist based on response to simple inputs
If a system does not have desired response, then it can be modified with control
SYSTEM

## Slide 3: Introduction to Control
Open-loop control
(feedforward control)
C(s)
P(s)
R(s)
“controller”
D(s)
+
+
“plant”
U(s)
U(s)+D(s)
Y(s)
summing
point
simple to design (plant inversion)
ignoring D(s), Y(s) = P(s)C(s)R(s)
therefore, C(s) = 1/P(s) provides
Y(s)=R(s)
cheap (no sensor needed)
not robust
Notes: Can’t account for disturbances
Don’t know if the output is different than predicted

## Slide 4: Introduction to Control
Closed-loop control
(feedback control)
C(s)
P(s)
R(s)
“controller”
D(s)
+
“plant”
U(s)
Y(s)
branching
point
more robust
more complicated/expensive
can cause a stable system to
become unstable
response can be slower
+
E(s)=
R(s)-Y(s)
+
-
Y(s)

## Slide 5: Block Diagram Reduction
Goal is to generate a transfer function from any given input to any given output of a block diagram

## Slide 6: Block Diagram Reduction
= GE
HY
Approach #1: Algebra
  Define a variable after each summing point
  Write equations and simplify
eliminate
E(s)
E

## Slide 7: Block Diagram Reduction
Approach #2: Block diagram manipulation
  Memorize rules for standard arrangements
Rule 1: Negative feedback
Rule 2: Positive feedback

## Slide 8: Block Diagram Reduction
Rule 3: Series
Rule 4: Parallel
=AG1G2
AG1
AG1
AG2
=AG1+AG2

## Slide 9: Example
DC motor torque control
θ
ea
θ
.
T
ia
eb
electrical
dynamics
mechanical
dynamics
controller
ia,des

## Slide 10
Does order of branching and summing points matter?
See table on page 495 of the book for more rules

## Slide 11
Does order of branching and summing points matter?
See table on page 495 of the book for more rules

## Slide 12
Θ
Ia,des

## Slide 13: Total Response
For linear systems with multiple inputs the total response is the sum of the individual contributions (property of superposition)
Assume only one input is non-zero at a time
Y

## Slide 14: Example
Total Response
Y

## Slide 15: Example
Another way to think
about the transfer function