## Slide 1: Lecture 16: Introduction to Control (Part II)
Illustrative cruise control example
Control requirements
Design by pole placement

## Slide 2: Cruise Control Example
F = control input
(road force, generated by engine indirectly)
v = output
(velocity of car)
f(v) = friction/drag force
Equation of Motion
F
f(v)
Notes: Note this is an oversimplification, but can still give insight

## Slide 3: Cruise Control Example
Transfer function
first-order
response
F
v

## Slide 4: Cruise Control Example
controller
plant
Response is stable (which is good)
Not robust to disturbances, uncertainties
May not be fast enough
How to make better? Add control!
Control law is f=Ke, applied force is proportional to the error
Notes: Sensor and actuator dynamics are neglected

## Slide 5: Cruise Control Example
Closed-loop transfer function


## Slide 6: Cruise Control Example
Making K larger makes system faster and DC gain closer to 1
  both are generally desirable
Any drawbacks?
  Eventually actuator will saturate
  Higher-order dynamics have been neglected (sensors, actuators), large K often will increase oscillation
  Large K can amplify unwanted inputs (like noise)
Can we do better by trying a more complicated controller?

## Slide 7: Cruise Control Example
In the preceding, the control was proportional to the error … called a P (proportional) controller
Can add terms for the integral of the error (I) and the derivative of the error (D)
Each term of the PID controller changes system performance in a different way

## Slide 8: Control Requirements
Approach to control design: Translate engineering specifications into control requirements, then design a controller to meet those specifications
Example transient specifications
  τ, Mp, tp, ts, tr
Example steady-state specifications
  Typically it is required that steady-state error be less than some amount, ess < 0.02
  Can use F.V.T. for different types of reference inputs

## Slide 9: Pole Placement
Poles of a system affect the time response
Choose controller gains (for ex. KP, KI, and KD) so that poles of the closed-loop system meet given requirements
If system is simple (first order, or second order) can employ algebra
Process is generally iterative

## Slide 10: Example
Find the closed-loop transfer function for a cruise control system with PI controller

## Slide 11: Example (continued)
With two parameters (KP and KI) can place poles of this second-order system anywhere we like (2 d.o.f.)
What is the effect of changing the control gains?
Notes: Mass = 1000 kg,
B = 50
Not exactly canonical … may need to do some tuning
U = 10 m/s step

## Slide 12: Example (continued)
Let m=5 and b=1. Choose KP and KI to achieve a settling time of 2 seconds and a peak time of 1 second.

## Slide 13: Example (continued)
Will the closed-loop system with this controller actually have a settling time of 2 seconds and a peak time of 1 second?