## Slide 1: Lecture 17: Introduction to Control (part III)
Example
PID Control
  Learn about the effect of tuning the P, I, and D gains
Steady-state error and system type

## Slide 2: Example
For the following system, design the PD controller (i.e. find KP and KD ) so that the closed-loop step response:
  settles to within 2% of its final value in less than 0.5 sec
  does not overshoot its final value more than 10%
  and for a unit ramp, the ss error is less than 0.02
Notes: Have values in km/hr, mph, for intuition

## Slide 3: Example (continued)
Find the closed-loop transfer function
Translate transient specifications into transfer function parameters and plot region of the complex plane where the closed-loop poles must be located
Notes: Mass = 1000 kg,
B = 50
Not exactly canonical … may need to do some tuning
U = 10 m/s step

## Slide 4: Example (continued)

## Slide 5: Example (continued)
Translate into requirements on KP and KD, also include steady-state requirement

## Slide 6: Example (continued)

## Slide 7: PID Control
PID controllers are ubiquitous
Very intuitive, easy to implement
Provide sophistication in that the control is based not only on the current error, but also the history of the error (integral of error) and the anticipated future error (derivative of error)

## Slide 8: PID Control
We will examine effect of PID control on a canonical 2nd order system to gain insight
Notes: Write on board

## Slide 9: P Control
Control effort is proportional to the amount of error
Cannot set ωn and ζ independently (only one d.o.f.)
Notes: Write transfer function on the board

## Slide 10: P Control
Effect on steady-state performance
Steady-state value for a unit step reference
larger Kp makes yss 1 … error goes to zero
y(t)
t
1
ss error

## Slide 11: PD Control
With derivative control, do not have to wait for error to get large before control action becomes large, control anticipates the error
Never use D control by itself, amplifies noise
Not canonical form, but trends are meaningful
Can place two poles anywhere (2 d.o.f.)

## Slide 12: PI Control
Control effort gets larger as error is accumulated
Cannot use canonical relations because third order with a zero, but tends to make system slower and more oscillatory
Notes: Write transfer function on the board

## Slide 13: PI Control
Effect on steady-state performance
Steady-state value for a unit step reference
therefore, steady-state error is zero for a step reference, even for small KI (just takes longer to reach steady state)
Notes: Write on the board

## Slide 14: PID Summary
Some intuition about the effect of the terms:
  Increasing KP: Same amount of error generates a proportionally larger amount of control … makes system faster, but overshoot more (less stable)
  Increasing KD: Allows controller to anticipate an increase in error, adds damping to the system (reduces overshoot) … can amplify noise
  Increasing KI: Control effort builds as error is integrated over time, helps reduce steady-state error, but can be slow to respond
  Note: these guidelines do not hold for all situations … look specifically at how poles are affected

## Slide 15: PID Control
For systems that are not canonical first or second order, need to use trial and error … can look for reduced-order approx
Following are helpful, though not always true
 | KP ↑ | KD ↑ | KI ↑
ss error | ↓ | --- | ↓
rise time | ↓ | --- | ?
settling time | --- | ↓ | ? (↑)
overshoot | ↑ | ↓ | ? (↑)

## Slide 16: System Type
In previous example, saw that adding integral control enabled our plant to track a step input with zero steady-state error
This trend is true in general, the presence of pure integrators (poles at the origin) reduce steady-state error to all types of inputs
The number of integrators is identified by a system’s type

## Slide 17: System Type
Definition: The number of poles at the origin in the forward path of a unity feedback control system is called the system’s type
Poles at origin can be in the controller or the plant

## Slide 18: System Type
Error for a unity-feedback system
 | Step Input r(t) = 1 | Ramp Input r(t) = t | Accel Input r(t) = ½t2
Type 0 system | nonzero | ∞ | ∞
Type 1 system | 0 | nonzero | ∞
Type 2 system | 0 | 0 | nonzero

## Slide 19: System Type
 | Step Input r(t) = 1 | Ramp Input r(t) = t | Accel Input r(t) = ½t2
Type 0 system |  | ∞ | ∞
Type 1 system | 0 |  | ∞
Type 2 system | 0 | 0 |