## Slide 1: Lecture 18: Root Locus Basics
Pole placement review and example
Angle and magnitude conditions
Rules for drawing the root locus

## Slide 2: Design for Transient Response
One approach to control design (choosing gains) is algebraic
For systems with closed-loop dynamics that match a known simple form
choose control gains to produce desired parameter values (place poles in desired location to achieve transient response)
This process is more difficult when you have a higher-order system, difficult to see the effect of gains on all poles

## Slide 3: Root Locus Introduction
Root locus is a graphical tool that shows how the locations of the poles of a closed-loop TF move as a parameter (like a control gain) is varied
Helpful for higher-order systems
Useful for finding approximate results quickly
Im
Re

## Slide 4: Example
Find the open-loop TF, the closed-loop TF, and the open-loop poles and zeros

## Slide 5: Example (continued)
Plot how the closed-loop poles change with KP
How does response change with KP? Does this match our earlier guidelines?
zeros = -2
poles = -1±j√(2)
Im
Re

## Slide 6: Root Locus Introduction
The graph of closed-loop pole locations in the previous example is the root locus plot
Can be drawn from the open-loop TF
In the following, we will learn an approximate procedure for drawing the root locus

## Slide 7: Angle and Magnitude Conditions
This will explain where our drawing procedure comes from
Closed-loop poles can be found from the open-loop TF, that is, from

## Slide 8: Angle and Magnitude Conditions
Assuming that a multiplicative parameter K is in G(s) or H(s), the previous equation becomes
Therefore, the root locus contains all points s for which this equation holds for some value of K

## Slide 9: Angle and Magnitude Conditions
plotted in the complex plane:
This translates into two conditions
Im
Re

## Slide 10: Angle and Magnitude Conditions
Note that
Any point s on root locus must satisfy angle condition
Therefore,

## Slide 11: Angle and Magnitude Conditions
Note: for complex conjugate zeros or poles and s on the real axis, the angles essentially cancel

## Slide 12: Angle and Magnitude Conditions
Based on the magnitude condition
  As K → 0, D → 0 and the locus approaches OL poles
  As K → ∞, N → 0 and the locus approaches OL zeros
In other words, branches of the root locus start at open-loop poles and end at open-loop zeros
Note: if more poles than zeros, then this includes (#poles - #zeros) “zeros” at infinity (asymptotes)

## Slide 13: Rules for Drawing the Root Locus
Locate OL poles and zeros in the s-plane
Determine root locus on the real axis
Approximate the asymptotes of the root locus
Approximate break-away and break-in points
Determine angles of departure and arrival
Find Imaginary axis crossings

## Slide 14: Example
Draw root locus for an OL TF of