## Slide 1: Lecture 21: Intro to Frequency Response
Review of time response techniques
Intro to the concept of frequency response
Intro to Bode plots and their construction

## Slide 2: Time Response Review
Previously, we have determined the time response of linear systems to arbitrary inputs and initial conditions
We have also studied the character of certain standard systems to certain simple inputs
  Used algebra and root locus to place dominant closed-loop poles to give desired time response
    τ, Mp, tp, ts, tr, etc.
SYSTEM

## Slide 3: Time Response Review
Advantage of pole-placement approach is that the time response can be affected directly, easiest for canonical systems
Disadvantage of the approach is that sometimes it is difficult to determine the effect of higher-order poles and of zeros, and how the system will respond to complex inputs

## Slide 4: Frequency Response Concept
Input sine waves of different frequencies and look at the output in steady state
If G(s) is linear and stable, a sinusoidal input will generate in steady state a scaled and shifted sinusoidal output of the same frequency
G(s)

## Slide 5: Frequency Response Concept
Two primary quantities of interest that have implications for system performance are:
  The scaling
  The phase shift
Important for designing controllers, filters, choosing sensors, designing mechanical systems, etc.
  = magnitude of G at s=jω
  = angle of G at s=jω

## Slide 6: Frequency Response Analysis
Attenuation may be
  desired: noise, disturbances
  undesired: commanded reference input
Amplification can destabilize a system (resonance)
Phase lag means information is delayed, can hurt performance and also destabilize a system

## Slide 7: Frequency Response Concept
Different ways to present this information:
  Bode diagram (two graphs)
    magnitude vs. frequency
    phase vs. frequency
  Nyquist plot
  magnitude vs. phase (polar)
  Nichols chart
  magnitude vs. phase (rectangular)

## Slide 8: Bode Diagram Example
Magnitude in decibels vs. frequency in rad/sec
Phase in degrees vs. frequency in rad/sec

## Slide 9: Other Examples
Nyquist plot
Nichols chart

## Slide 10: How to Plot a Bode Diagram
Approach #1: Point by Point
Substitute s=jω into G(s) and calculate magnitude and phase for a series of different frequencies ω
where

## Slide 11: How to Plot a Bode Diagram
Approach #2: Use asymptotic approximations
Plot straight-line approx of components, then add
Ex.
can add Bode plots because of mathematical props

## Slide 12: How to Plot a Bode Diagram
Need a library of components
Constant gain (K)
ω(rad/sec)
M(dB)
ω(rad/sec)
φ(deg)

## Slide 13: How to Plot a Bode Diagram
2. Differentiator (s)
ω(rad/sec)
M(dB)
ω(rad/sec)
φ(deg)

## Slide 14: How to Plot a Bode Diagram
3. Integrator (1/s)
ω(rad/sec)
M(dB)
ω(rad/sec)
φ(deg)

## Slide 15: How to Plot a Bode Diagram
4. Simple zero (Ts+1)
ω(rad/sec)
M(dB)
ω(rad/sec)
φ(deg)

## Slide 16: How to Plot a Bode Diagram
5. Simple pole (1/(Ts+1))
ω(rad/sec)
M(dB)
ω(rad/sec)
φ(deg)

## Slide 17: How to Plot a Bode Diagram
Will do complex poles and zeros later (2nd order)
Approach #2:
  Put into Bode form
  Sketch straight line approximations
  Add graphs
  Try to approximate curves

## Slide 18: Example
Sketch Bode diagram for
  Put into Bode form
  Sketch components
a
b
c

## Slide 19: Example (continued)
M(dB)
φ(deg)
M(dB)
φ(deg)

## Slide 20: Sketch Requirements
Magnitude plot
Frequency where slope changes
Slope of each line segment
Magnitude of at least one frequency
Phase plot
Frequency where slope changes
Do not need to identify slopes, but magnitudes must be relative
Limiting phase as frequency goes to zero and infinity
Make sure to include the following elements in your hand sketches of Bode diagrams