## Slide 1: Lecture 24: More Advanced Architectures
Different architectures
  Two degrees-of-freedom control
  Feedforward control
  Addressing multiple inputs
  Addressing complexity with multiple loops
More design with MATLAB

## Slide 2: Different Architectures
So far we have primarily considered a negative feedback architecture with one loop and our controller in the forward path
Many other architectures exist

## Slide 3: Two-Degrees-of-Freedom Control
Allows two of (Gyr, Gyn, Gyd) to be designed independently

## Slide 4: Feedforward Compensator
Feedforward action can be used to correct for “known” disturbances
C(s) is designed by model inversion, can be static or dynamic
θ
.
T
ia,des
ea
eb
ia
TL
TL,est

## Slide 5: Feedforward Compensator
Pre-compensation can also be used to cancel undesired dynamics of the plant and to scale the steady-state output
Pre-compensator can speed response, but is susceptible to errors in the model and disturbances
“Error” is distorted by K(s) and errors in K(s) aren’t corrected by the feedback

## Slide 6: Feedforward Compensator
Implementing the feedforward term as follows avoids these problems
Note, this is one of our 2-dof controllers

## Slide 7: Multiple Inputs
We have primarily designed control for single input single output (SISO) systems
When we had multiple inputs, we could examine the response to each input separately if the system was linear
If inputs are coupled in a nonlinear manner, we can use heuristics to decouple them

## Slide 8: Example
Separately excited DC motor control
  Control both armature current and magnetic field strength
ea
ia
ef
if
ia,des
if,des
Tdes
ω

## Slide 9: Example
Permanent magnet synchronous machine (traction motor) control often uses an approach called Vector Control or Field Orientation Control to emulate the previous case
Employs DQ modeling

## Slide 10: Multiple Loops
Using nested controllers can help reduce the complexity of the design for higher-order systems if the dynamics can be de-coupled based on speed
Using a single controller can limit speed of response due to slow (dominant) dynamics

## Slide 11: Multiple Loops
Approach:
    Design control for the fast inner loop
    Treat inner loop as static, then design control for slow outer loop
    Can continue beyond two nested loops
torque (current)
speed
desired
speed
desired
torque
θ
.
T
ia

## Slide 12: Example
Section 8-7 of Mohan, Electric Drives
Step 1: Design Fast Inner Loop (the current loop)
Approach used: place zero of controller to cancel slow pole of the plant, then choose gain to achieve gain crossover frequency a decade or two below power electronics switching frequency
ia,des
ia

## Slide 13: Example (cont)
System Parameter | Value
Ra | 2.0 Ω
La | 5.2 mH
J | 152x10-6 kg·m2
b | 0
Ke | 0.1 V/rad/s
K | 0.1 Nm/A

## Slide 14: Example (cont)
Magnitude plot of
Desire Kc so that gain crossover frequency is one to two decades below switching frequency, in this case fs=200,000 rad/sec

## Slide 15: Example (cont)
Controller for the current loop
Resulting open-loop magnitude plot

## Slide 16: Example (cont)
Step 2: Treat inner loop as a static gain then design slow outer loop (speed loop)
desired
speed
θ
.
current
loop

## Slide 17: Example (cont)
Since b=0,
Desire to place gain crossover frequency one decade below crossover of inner current loop
Desire to achieve reasonable phase margin, ≈ 60 degrees

## Slide 18: Example (cont)
Will use SISO Design tool in MATLAB